# 130C-14

MEASURING WITH A RULER

1/16th INCH SCALE

1/16"

1/4"

7/16"

11/16"

1"

1 1/16"

1 1/8"

1 1/4"

1 1/2"

1 3/4"

1 7/8"

2 3/16"

2 7/16"

1/8th INCH SCALE

3/8"

5/8"

7/8"

1 1/8"

1 5/8"

# 130C-15

# MEASURING WITH A RULER, WORKSHEET

A	       B    C	  D    		E      	F       G	H        I	   J

K		   L			M	       N			O

Write down the measurements for the location at each letter.

1. A=________		  6. F=________		11. K=________

2. B=________		  7. G=________		12.  L=________

3. C=________		  8. H=________		13. M=________

4. D=________		  9.  I=________		14.  N=________

5. E=________		10.  J=________		15.  O=________

Measure lines 16 through 20 to the nearest 1/16th and record the results.

16. 										16=________

17.										17=________

18.										18=________

19.										19=________

20.										20=________

# 130C-16

# READING THE MICROMETER

Picture shows only the sleeve and part of the thimble

Measure to the nearest one thousandth.

0	   1       2	    25

## Example A

0 – 1 inch micrometer				    20

Sleeve Reading:	0.200 inch

0.025 inch

0.025 inch

0.025 inch

Thimble Reading:	0.023 inch

## Total Reading:		0.298 inch

Measure to the nearest one thousandth.

4	     5        6	    20

Example B

1 – 2 inch micrometer

15

1 – 2 inch micrometer =	1.000 inch

Sleeve Reading:		0.600 inch

0.025 inch

0.025 inch

Thimble Reading:		0.018 inch

## Total Reading:			1.668 inches

### Top View, Vernier Scale

Measure to the nearest ten thousandth.

7        8       9	    5		      9

Example C 								    7		            15

2 – 3 inch micrometer				    25		      5

2 – 3 inch micrometer:	2.0000 inch

Sleeve Reading:		0.9000 inch

0.0250 inch

0.0250 inch

## Thimble Reading:		0.0010 inch

## Vernier scale:			0.0009 inch

Total Reading:			2.9519 inches

# 130C-17

MICROMETER WORKSHEET

Fill in the correct measurement in the blank.

Measure to the nearest one thousandth.

0 – 1 inch	       6	     7       8        9

20			1. ________

0 – 1 inch	     6	   7       8        9         25

2. ________

20

1 – 2 inch	       3	     4       5        6       25

3. ________

5

1 – 2 inch 	            5        6        7

4. ________

25

0 – 1 inch 	       2	     3       4        5

25			5. ________

2 – 3 inch   	          1        2       3       4     20

6. ________

0 – 1 inch 	          7        8       9       0

7. ________

25

MICROMETER READING WORKSHEET

Micrometer Size						Reading

0 to 1 inch						___________________

2 to 3 inch						____________________

0 to 1 inch						____________________

4 to 5 inch						____________________

3 to 4 inch						____________________

10 to 11 inch						____________________

1 to 2 inch						____________________

# Text boxes

2

3

3

2

1

1

2

3

1

1

3

2

3

2

1

0

20

0

5

0

10

1

2

3

0

10

15

1

2

3

4

0

15

20

1

0

20

0

1

2

0

10

15

1

2

3

4

0

15

20